## Slide 1: Light Electric Vehicle Propulsion
Ed Benjamin

## Slide 2: Who is this guy Benjamin?
Currently VP Light Transport WaveCrest Laboratories
Since 1995, President of CycleElectric Consulting Group – focusing on electric bikes, scooters, motor-scooters.
Co author of Electric Bikes World Wide Reports 2004 (With Dr. Jamerson)
Contributor to most industry trade journals on light electric vehicles and bicycles.

## Slide 3: Why would anyone be interested in light electric vehicle propulsion
2004 sales of LEVs and products using the same propulsion components (light scooters, robots, bicycles, motor scooters, motorcycles, etc.) more than 13 million pieces.
The potential is much larger…

## Slide 4
Bicycles are primary transportation for billions of people around the world – and no one likes to pedal to work.
  Over 130 million bicycles are sold every year
  Over 10 million electric bicycles will be sold in 2005
43 million gasoline-powered scooters mopeds, and motor cycles are sold every year
  They are a major source of air pollution, especially in developing nations. Electric is an attractive alternative.

## Slide 5: All of these folks are potential buyers of LEVs

## Slide 6: LEV = Electric Bicycle, Motorscooter, Light Scooter
Electric Bicycles – about 10 million will be sold in next 12 months world wide.
Electric Motor Scooters – about 25,000 will be sold in next 12 months.
Light Scooters – 3 to 5 million depending upon some pending regulations.

## Slide 7: China 10 million units total all styles
350 makers – 200 to 450 US $ Retail

## Slide 8: China
Transportation for the upscale worker and middle managers

## Slide 9: Japan – 200,000 Units
Honda
Sony
National / Panasonic and Yamaha are market leaders 700 US to 1,000 US $ Retail
Transportation for housewives and older people

## Slide 10: EU – 95,000 Units
Prima Power Bike, Italy
Aprillia Enjoy, Italy
Including Chinese imports – 400 US to 2700 US$
Transport and Recreation – mostly older users

## Slide 11: USA – 65,000 Units
Lee Iacocca – EV Global
WaveCrest Tidal Force
Recreational Users
Including Chinese imports - 300 US to 3300 US$

## Slide 12: Specialty Markets World Wide

## Slide 13: Typical Electric Bike Specifications
Depending on regulatory environment – speeds from 16Kph to 45 Kph. USA = 20 mph.
Range of 10 – 40 miles, most are about 20 miles.
Weight of 40 – 120 lbs, most are 65-85 lbs.
Climbing ability from 0% grade to 15%

## Slide 14: Light Electric Scooters
USA will buy millions of these, but most of the rest of the world regards them as undesirable toys and they are regulated as “motor vehicles” and often forbidden use on roadways.
This trend, frankly, exists in the USA as well.

## Slide 15: Light Scooters
Most are Chinese made imports ranging from 150 to 900 US$ retail.

## Slide 16: Typical Light Scooter Specifications
100 – 750 watt brush and brushless permanent magnet DC motors.
Both cylindrical and hub motors used
Range 8-20 miles
Weight 20-100 lbs.

## Slide 17: Electric Motor Scooters
Equivelant in performance to 29-50cc Gasoline “Vespa” and “Moped” style vehicles.
Strong encouragement programs in many countries.
Energy storage is a big issue.

## Slide 18: Electric Motor Scooter

## Slide 19: Most LEVs are Battery Electric
Most common energy storage is Pb, followed by NiMH.
A few Li-Ion and Li-Poly bikes exist in production.
Experiments are underway with hybrids, Zinc Air, and fuel cells.
Heavy use of Ni-Cad in Japan and EU is now history due to regulatory restrictions.

## Slide 20: Most Vehicle Builders Prefer a complete propulsion system
Most vehicle builders come from bicycle or motorcycle business. They do not have the experience or knowledge to integrate propulsion system themselves – they want to buy a complete solution.
Complete solutions include energy source (battery), controller and motor.

## Slide 21: Drive Systems
150 - 250 watt hub motors – gear reduction and direct drive – most common in China.
250 watt bottom bracket drive used in Japan.
250 to 600 watt motors in a variety of configurations used in EU.
250 – 1,000 watt motors in a variety of configurations used in USA.

## Slide 22: Chinese Hub Motor 150 – 250 watts, direct or gear reduction
Low cost, not consistent in quality or performance, more than 70 makers, “good enough” for the China market and low price export market.

## Slide 23: German Hub Motors
Heinzmann is dominant producer – 250 – 750 watt gear reduction hub motors. Quite good, not cheap.

## Slide 24: Japanese Drive Systems
250 watt, designed for Japanese regulations – proportional drive PAS paradigm.
Some hub motors are used, including an American designed model for Sanyo.

## Slide 25: Many designs use conventional motors…
2 KW motor driving a belt and sprocket gear reduction…

## Slide 26: There are a variety of different ideas….

## Slide 27: Hub Motors have the advantage -
Hub motors easily fit on existing frames and platforms.
Hub motors use a space that is otherwise not used at all.
This applies to almost all LEVs.
There seems to be a nearly universal intuitive acceptance of hub motors by consumers.

## Slide 28: High Performance Hub Motors
Heat dissipation and durability are major issues – also noise, cost and serviceability.

## Slide 29: USA – WaveCrest
250 – 1,000 watt hub motor on rear, battery in front hub, silent, brushless DC PM motors. Unique design.

## Slide 30: Important issues for consumers
In rough order of importance:
Cost
Noise
Torque
Reliability
Weight
Efficiency

## Slide 31: Different priorities
Military and Police – silence, range, speed
Industrial – range, reliability
Some EU markets – reliability
Photos

## Slide 32: Major Suppliers of Motors and Propulsion Systems
More than 70 makers in China
National, Sanyo, Yamaha
Heinzmann, Schachner
WaveCrest
MAC / BMC
Koll Morgan
TDCM
Many others

## Slide 33: Opportunities for future
Smaller size
More efficient
Lower cost
Better torque characteristics – only one design that is satisfactory at this time.
More durable.
Better controller characteristics
Better controller reliability

## Slide 34: Emerging markets for LEV size propulsion systems
Robots
Industrial carts
Personal mobility
Trailers
Others

## Slide 35: Not just about motors…
Most customers for motors are the vehicle makers – who would prefer a one stop source for the complete system including motor, energy storage, controls, user interface and wiring harness. (All at a very low cost … of course!)
A correct strategy for a vehicle maker is to demand a complete system from one supplier – avoiding the “it is the software guy“– says the hardware guy. “No! – It is the hardware” says the software guy.

## Slide 36: Controls
The majority of current motor controls for LEVs have been improvisations controlled by price points and created by people who were not expert in high current applications.
Reliability, and the “feel” of the controller are major sources of consumer dissatisfaction.

## Slide 37: Energy Storage
The limitation to all electric vehicles is the method and density of energy storage.
A propulsion system supplier needs expertise in batteries and Battery Management Systems as a minimum.
Better is to have expertise in batteries, BMS, small hybrid systems, and fuel cells.

## Slide 38: Thanks!
Questions?
This presentation will be posted at www.CycleElectric.com and www.wavecrestlabs.com within 2 weeks.
Questions emailed to ed.benjamin@wavecrestlabs.com will be answered as best as I can and referred to other experts if appropriate.