## Slide 1
Akustički dizajn prostorija
Apsorberi zvuka

## Slide 2
Primena apsorbera zvuka
Kontrola vremena reverberacije
Smanjenne nivoa buke u bučnim prostorijama
Prigušenje frekvencija rezonansi u akustički malim prostorijama
Eliminisanje kasnih refleksija (eho)
Povećanje akustičke izolacije između prostorija
Smanjenje nivoa buke u installacionim kanalima i cevima

## Slide 3: Apsorberi zvuka
Podela prema načinu rada:
porozni rezonatorski panelni

## Slide 4
Apsorberi zvuka
Karakteristika koeficijenta apsorpcije i frekvencijska područja efikasnog rada

## Slide 5
Malcolm J. Crocker, HANDBOOK OF NOISE AND VIBRATION CONTROL, John Wiley & Sons, Inc., 2007.

## Slide 6
Typically, solid materials and porous absorbers show a
steady increase in the absorption coefficient as the frequency increases. Masonry
walls, either plain or plastered, are typical examples of the former, and any material
with an open cellular or fibrous structure, for example mineral wool quilt, is an
example of the latter.
Cavity absorbers are sometimes individually designed and made to absorb at a specific frequency, but they are more often created by forming perforations in a sheet material.

## Slide 8: Apsorberi zvuka

## Slide 9
Porozni apsorberi

## Slide 10
Porozni apsorberi
Prostiranje zvuka kroz pore poroznog materijala dovodi do gubitka dela akustičke energije.
Gubitak nastaje usled viskoznog trenja u porama materijala i termičkog efekta.
Da bi mehanizam apsorpcije bio efikasan pore moraju biti međusobno povezane – struktura sa otvorenim porama. Ovakvi apsorpcioni materijali se mogu “produvati”.

## Slide 11
Porozni apsorberi
Materijal sa zatvornim porama
Materijal sa otvornim porama – dobar apsorber

## Slide 13
Porozni apsorberi
Mineralna vuna
Akustička pena
Vrste materijala

## Slide 14
Porozni apsorberi
Vrste materijala
Reciklirani materijali
odeća, pena, drvo, metal. plastika, guma
Azmafon - fino raščešljana pamučna vlakana povezana smolom

## Slide 15
Porozni apsorberi
Apsorpcija beskonačno debelog sloja
Za mineralnu vunu potreban je sloj debljine oko 90 cm
 - poroznost materijala

## Slide 16
Porozni apsorberi
Apsorpcija sloja debljine 11 cm (morska pena)
Strmiji pad na niskim frekvencijama,
neravna karakteristika

## Slide 17
Porozni apsorberi
Uticaj debljine materijala
Kod tankog sloja deo energije se reflektuje od zida

## Slide 19
Porozni apsorberi
Podaci proizvođača - Uticaj debljine materijala

## Slide 20
Mineralna vuna otp strujanja 10000 Pas/m2
J. Pfretzschner, R. Mª. Rodríguez
Acoustical Absorption and Critical Thickness
Instituto de Acústica-CSIC. C/ Serrano, 144. 28006 Madrid-Spain

## Slide 21
Porozni apsorberi
Uticaj položaja materijala u odnosu na zid (reflektujuću površinu)

## Slide 22
Porozni apsorberi
frekvencija - 950 Hz
četvrtina talasne dužine – 9 cm
Tanak sloj tkanine na različitim rastojanjima od zida

## Slide 23
Porozni apsorberi
Tanak sloj tkanine udaljen 9 cm od zida

## Slide 24: Porozni apsorberi
Porozni apsorber debljine 2,5 cm na različitim rastojanjima od zida.

## Slide 25
Porozni apsorberi
Obloga ispred apsorpcionog materijala – tanka folija
Koeficijent transmisije 
 (%) | f ms
5 | 808
10 | 556
20 | 371
30 | 283
40 | 227
50 | 185
60 | 151
70 | 121
80 | 93
90 | 62
95 | 42

## Slide 26
Porozni apsorberi
Zavese
Uticaj težine [Beranek]
Uticaj nabiranja [Harris]

## Slide 27
Porozni apsorberi
Tepisi
Apsorpcija zavisi od tipa tepiha i njegove osnove [Beranek]

## Slide 28
Akustički razonatori

## Slide 29
Akustički rezonatori
U praktičnoj primeni se koriste kao:
pojedinačni razonatori (razmešteni daleko jedan od drugog) – Helmholcovi rezonatori
spojeni rezonatorski sistemi
rezonatorski sistemi sa procepom

## Slide 30
Helmholc-ov rezonator
Efekat unošenja apsorpcionog materijala u komoru
frekvencija
rezonanse
ekvivalentna dužina vrata

## Slide 31
Perforisana ploča
Spojeni akustički razonatori
frekvencija rezonanse
procenat perforacije

## Slide 32
Perforisana ploča - Izračunavanje procenta perforacije 
Spojeni akustički razonatori

## Slide 33
D. Bies, C Hansen, Engineering noise control, 3-rd ed., Spon Press, 2003.

## Slide 34
Perforisana ploča - primer iz prakse
Spojeni akustički razonatori

## Slide 35
Akustički razonatori sa procepom

## Slide 36
Akustički razonatori sa procepom

## Slide 37
Akustički razonatori sa procepom

## Slide 38
Akustički razonatori – položaj apsorpcionog materijala
materijal najmanje efikasan, mala brzina čestica
materijal efikasniji ali je aktivan mali deo materijala koji otpada na otvore
ceo materijal efikasan ali mora biti nešto deblji nego u slučaju b).

## Slide 39
Višestruki akustički razonatori

## Slide 40
Akustički razonatori – praktični primer 1

## Slide 41
Akustički razonatori– praktični primer 2

## Slide 42
Akustički razonatori– praktični primer 3

## Slide 43
Akustički razonatori– praktični primer 4